## Slide 1
QC
REAL-TIME INDUSTRIAL DEFECT
DETECTION SYSTEM
AI-Powered Manufacturing Quality Control · NEU Surface Defects · YOLOv8
72.5%
MAP@0.50
0.394
MAP@0.50:0.95
61.6 FPS
ONNX CPU EDGE
6
DEFECT CLASSES
All figures measured on the delivered system — NEU-DET validation set, GTX 1650 / CPU

## Slide 2
AGENDA
What this presentation covers
01
Problem & impact
why automated surface inspection
02
Dataset
NEU-DET: 1,800 images, 6 defect classes
03
Data pipeline
VOC→YOLO conversion, validation, augmentation
04
Model & experiments
YOLOv8n training, 4 measured experiments
05
Results
mAP 72.5 / 39.4, per-class AP, error analysis
06
Edge optimisation
ONNX Runtime, 62 FPS on CPU, backend fallback
07
Quality control
PASS/REJECT, temporal confirmation, PLC simulation
08
System & monitoring
FastAPI, dashboard, SQLite, Prometheus, Grafana, Docker
09
Testing, limitations, demo
53 tests, honest constraints, live demo flow
02

## Slide 3
PROBLEM STATEMENT
Manual steel inspection is slow, inconsistent and costly
Human visual inspection of rolled steel is fatiguing and subjective — quality varies across shifts and inspectors
Escaped defects become manufacturing waste or reach end customers: rework, returns, reputation damage
Rule-based machine vision (fixed thresholds) cannot handle the visual variety of the six NEU defect classes
Deep learning object detection learns defect appearance directly from labelled images and runs in milliseconds
PROJECT GOAL
Minimise manufacturing waste and prevent defective products from reaching end consumers — with consistent, unbiased, high-throughput quality control at the edge.
No cloud. No paid services. Runs on a laptop-class machine next to the production line.
03

## Slide 4
SYSTEM OVERVIEW
From camera frame to sorting decision — in milliseconds
1
Capture
webcam / video / RTSP
(OpenCV)
▸
2
Preprocess
letterbox 320×320
RGB, /255
▸
3
Infer
TensorRT ▸ ONNX ▸
PyTorch (auto, load-validated)
▸
4
Detect
6 classes · boxes ·
confidence
▸
5
Decide
temporal 2-of-3 →
PASS / REJECT
▸
6
Act & record
PLC signal · SQLite ·
metrics · dashboard
PARALLEL MONITORING CHAIN
FastAPI
model loaded once,
shared by all requests
▸
Dashboard
10-page control-room UI
(live MJPEG feed)
▸
SQLite
every inspection recorded,
filterable history
▸
Prometheus
13 metric families
scraped every 5 s
▸
Grafana
auto-provisioned
datasource + dashboard
Measured live snapshot: 25.9 ms total pipeline latency (13.7 ms inference) on ONNX Runtime CPU
04

## Slide 5
DATASET
NEU Surface Defect Database (NEU-DET)
1,800
IMAGES
grayscale 200×200 px
4,189
BOUNDING BOXES
Pascal VOC XML
1,440 / 360
TRAIN / VAL
built-in split
6
DEFECT CLASSES
balanced per image count
Class | Train objects | Val objects | Appearance
crazing | 524 | 162 | networks of fine cracks
inclusion | 852 | 159 | embedded foreign material
patches | 688 | 193 | patch-like surface damage
pitted_surface | 345 | 87 | small pits on the surface
rolled-in_scale | 496 | 132 | oxide scale rolled into surface
scratches | 427 | 121 | linear scratches
KEY FACTS
1,033 / 1,439 train images have multiple defects
2.47× class imbalance (inclusion vs pitted_surface)
No normal (defect-free) images exist in NEU-DET
Archive preserved untouched; XMLs never modified
Source: NEU Surface Defect Database (NEU-DET), verified by our inspection scripts
05

## Slide 6
DATA PIPELINE
Verified conversion — no silent data loss
1
Extract
archive preserved untouched;
raw data read-only
1,800 images
2
Convert VOC→YOLO
normalised class cx cy w h;
degenerate boxes rejected
4,186 boxes kept
3
Validate
ids 0–5, coords in [0,1],
complete image-label pairs
100% valid
4
Visual check
YOLO boxes re-drawn and
compared to source VOC
IoU ≥ 0.85 every box
5
Augment
online: mosaic, flips, ≤5° rotate;
offline: CLAHE/gamma/noise
bbox-safe only
WHY THIS MATTERS
A single mis-converted bounding box silently teaches the model wrong locations. Every one of the 4,186 labels was machine-validated and 120 samples were visually compared against the original Pascal-VOC annotations — zero shift or distortion detected.
06

## Slide 7
MODEL & TRAINING
YOLOv8n — chosen for the edge, tuned for NEU
Setting | Value
Architecture | YOLOv8n (3.0 M params, 8.1 GFLOPs) — COCO-pretrained transfer
Image size | 320 px (native source is 200×200 — 640 blurrs fine texture)
Epochs / batch | 60 / 16, early-stopping patience 12
Augmentation | mosaic, h-flip 0.5, ≤5° rotation, HSV-V 0.2
Optimizer | AdamW, lr0 = 0.01 (auto strategy)
Hardware | GTX 1650 4 GB (CUDA 12.1), Windows-safe workers = 0
WHY 320 px? (measured)
640 px
mAP50 0.671
320 px
mAP50 0.725
Upscaling 200 px source to 640 blurs defect texture and costs 4× compute — the smaller native-scale input trains faster AND scores higher.
Windows/CUDA pitfalls solved: torch cu126 vs driver 528.49 → cu121; dataloader spawn + CUDA crash → workers = 0; VRAM thrash at batch 16 → batch 8 (640) / 16 (320).
07

## Slide 8
EXPERIMENTS
Four measured runs — the decision was evidence-driven
Chart: 
| baseline 640px | 320px (final) | no-mosaic 320px | yolov8s 320px
mAP@0.50:0.95 | 0.329 | 0.394 | 0.36 | 0.316
DECISION LOG
baseline 640 px
mAP50 0.671 · P 0.600 · R 0.661 — converged, VRAM thrash
320 px (final)
mAP50 0.725 · P 0.686 · R 0.686 — best on every key metric
mosaic off
mAP50 0.705 — augmentation tuning rejected mosaic removal
yolov8s
mAP50 0.674, 3.4× larger — rejected (small dataset favours nano)
Source: outputs/evaluation/experiment_comparison.csv — every run logged with config + metrics
08

## Slide 9
FINAL RESULTS
YOLOv8n @ 320 px — 60 epochs — evaluated fresh on the validation set
72.5%
MAP@0.50
val 360 images / 854 boxes
39.4%
MAP@0.50:0.95
strict IoU average
68.6%
PRECISION
equal to recall — balanced
68.6%
RECALL
F1 = 0.686
Chart: 
| patches | scratches | inclusion | pitted surf. | crazing | rolled-in scale
AP@0.50 | 0.923 | 0.837 | 0.825 | 0.792 | 0.487 | 0.486
READING THE RESULTS
Patches, scratches, inclusion all exceed 0.82 AP50 — production-ready on those classes
Crazing & rolled-in scale are the weak pair (fine, low-contrast textures) — 0.49 AP50
Confusion concentrates inside the crazing / pitted / scale texture family
Source: outputs/evaluation/final/metrics.json + per_class_metrics.csv — measured, not estimated
09

## Slide 10
ERROR ANALYSIS & THRESHOLD TUNING
Choosing the operating point for quality control
ERROR PROFILE (360 val images, conf 0.35)
561
TRUE POSITIVES
258
FALSE POSITIVES
293
FALSE NEGATIVES
Most missed: crazing (95) · rolled-in scale (65). Most false alarms: scratches (68), crazing (57).
Confidence | Precision | Recall | F1 | Use case
0.25 | 0.683 | 0.685 | 0.684 | recall-priority QC
0.35 ◄ selected | 0.754 | 0.639 | 0.692 | best F1, balanced
0.50 | 0.843 | 0.539 | 0.657 | precision-priority
QUALITY-CONTROL LOGIC
Missing a real defect costs more than a false alarm — so the default (0.35) does not maximise precision. Temporal confirmation (2 of last 3 frames) prevents one noisy frame from rejecting a part, and a 2 s PLC debounce turns 12 consecutive defect frames into exactly 1 reject command (measured decision latency 0.3–0.6 ms).
Source: outputs/evaluation/final/threshold_analysis.json — single-pass multi-threshold evaluation
10

## Slide 11
EDGE OPTIMISATION
Same model, same inputs — measured on this machine
Chart: 
| PyTorch CUDA FP32 | PyTorch CUDA FP16 | ONNX Runtime CPU | PyTorch CPU FP32
median latency (ms) | 12.8 | 13.5 | 16.2 | 28
WHY ONNX RUNTIME CPU IS THE DEFAULT
p95 ≈ median (17.5 vs 16.2 ms) — CUDA here shows rare VRAM-stall spikes (WDDM shared GPU)
identical detections to PyTorch: 100% class agreement, box IoU 1.0, Δconf 0.0
no GPU dependency — runs on any factory PC
61.6 FPS sustained, stable over 320-frame run (+2.6 MB RSS)
TensorRT: optional — auto-detected if an engine exists; reported unavailable here
Source: outputs/evaluation/edge_benchmark.csv + onnx_consistency.json — 100 iterations per backend, warm-up excluded
11

## Slide 12
QUALITY CONTROL & PLC
Industrial sorting logic, simulated safely
PASS / REJECT
REJECT iff any defect ≥ 0.35 confidence.
Per-defect severity: LOW→CRITICAL
(class weight + confidence + area + count)
Temporal confirmation
REJECT needs defects in ≥2 of the last
3 frames — a single noisy frame can
never reject a part (unit-tested).
PLC debounce
2 s cooldown: one continuous defect =
one reject command (12 defect frames
→ exactly 1 command, measured live).
Decision latency
confirmed decision → PLC dispatch
measured and exposed as a metric:
0.3–0.6 ms in live verification.
PLC is clearly labelled SIMULATED in the UI — a PLCAdapter interface with a Modbus TCP skeleton makes a real controller a drop-in replacement.
12

## Slide 13
SOFTWARE SYSTEM
FastAPI backend + industrial control-room dashboard
BACKEND (FASTAPI)
Model loaded once at startup — shared by every request and camera frame
POST /api/detect/image · /api/detect/video (multipart, validated)
MJPEG live stream (/api/video_feed) + camera start/stop
SQLite history: filters (status/class/severity), pagination, aggregates
Clean 400/413/422 errors — no stack traces reach clients
OpenAPI docs auto-generated at /docs
DASHBOARD — 10 PAGES, ZERO FAKE DATA
Overview: real KPIs, 6 charts, recent events
Live Inspection: MJPEG feed, boxes + severity, PLC panel
Image Inspection: drag&drop + one-click NEU sample, download link
History: filters + pagination · Analytics: 6 real charts
Model Performance: measured metrics + edge benchmark table
Dataset Explorer · System Health · Settings
Every displayed figure comes from the API, SQLite, evaluation artifacts, benchmark files or live state — empty states are explicit.
13

## Slide 14
MONITORING & DEPLOYMENT
Production habits applied to a college project
Prometheus
13 metric families on /metrics: requests, detections by class,
PASS/REJECT counters, latency histogram, camera status/uptime/FPS,
frames processed, PLC events + decision latency, API errors
Grafana
auto-provisioned datasource + dashboard JSON; live verification:
detection counter observed by Prometheus scrape (target UP)
Docker
docker compose up -d → app + prometheus + grafana verified
end-to-end (CPU torch inside the image; models mounted as volumes)
Native Windows
one-command local run (uvicorn) — cold-start tested from a
clean terminal; identical behaviour to the container
Verified live: a real detection through the containerised app incremented defect_detection_requests_total observed by the Prometheus scrape.
14

## Slide 15
TESTING & QUALITY
53 automated tests + full manual verification
53 / 53
PYTEST PASSED
0 failed · 0 skipped
20 / 20
API CHECKS
endpoints + invalid inputs
10 / 10
DASHBOARD PAGES
real browser walkthrough
WHAT THE TESTS COVER
Data: VOC→YOLO maths, bbox normalisation bounds, degenerate-box rejection, class mapping
Decisions: PASS/REJECT rules, severity grading, temporal validator (noise/persistence/slide/disable), PLC debounce & cooldown
Robustness: corrupt-ONNX → PyTorch fallback, all-models-missing error, model-file validation, DB round-trip
API: health/status/classes/metrics schemas, invalid uploads (text/corrupt/missing), malformed requests
15

## Slide 16
LIMITATIONS
Stated honestly — because credibility matters
1
No defect-free samples
NEU-DET contains only defective images — PASS decisions (absence of detection) are unvalidated against pristine surfaces
2
Single-dataset model
trained & evaluated only on NEU; real-plant lighting/materials require fine-tuning — not production-certified
3
Simulated PLC
sorting is simulated through an adapter; Modbus TCP skeleton included but untested on hardware
4
Environment bounds
TensorRT not installed (optional, fallback verified) · RTSP accepted but untested against a live camera
5
Weak classes
crazing and rolled-in scale sit at ≈0.49 AP50 — fine low-contrast textures remain hard
16

## Slide 17
CONCLUSION
A complete, measured, demonstrable system
DELIVERED
Custom 6-class defect detector: mAP50 0.725 @ 320 px, 6.2 MB
62 FPS CPU inference via ONNX — edge-ready without a GPU
Image / video / live inspection with PASS/REJECT QC
Temporal confirmation + debounced PLC simulation
Dashboard, SQLite history, Prometheus + Grafana monitoring
Docker deployment verified end-to-end; 53 tests green
NEXT STEPS
Collect defect-free surfaces; validate PASS decisions on pristine steel
Targeted augmentation + thresholds for crazing / rolled-in scale
TensorRT INT8 with a proper calibration set
Live Modbus TCP PLC over the existing adapter interface
Multi-camera line support with frame-queue load balancing
17

## Slide 18
LIVE DEMO
Seven minutes, in this order
1
Open dashboard
Overview loads with real KPIs — no camera needed
2
Dataset Explorer
click Scratches: real NEU images + ground-truth boxes
3
Image Inspection
Load Sample → REJECT banner, confidence + severity cards
4
Live Inspection
start camera: boxes, FPS, latency breakdown, PASS/REJECT
5
PLC panel
SIMULATED badge, reject signal, decision latency 0.3–0.6 ms
6
Model Performance
measured mAP / per-class AP / edge benchmark table
7
Health + /metrics
services, CPU/RAM/GPU, then Prometheus + Grafana URLs
Demo is webcam-independent — steps 2, 3, 6, 7 run entirely from real recorded data.
18

## Slide 19
Minimise waste.
Stop defects at the line.
Inspect at the edge.
Real-Time Industrial Defect Detection System — trained on NEU-DET, evaluated at 72.5% mAP@0.50,
deployed locally and in Docker, verified by 53 automated tests.
Thank you — questions welcome
Project: D:\NEU · Documentation: README.md / PROJECT_DOCUMENTATION.md / FINAL_TEST_REPORT.md